## Slide 1
CFD CWM
Luca di Mare
St John’s College
Oxford Thermofluids Institute
Engineering Science Department
University of Oxford

## Slide 2
Introduction
This document contains information about the CWM
  Logistics/housekeeping
  Schedule for the week
  Learning objectives
  Briefs for the final assessment
We will use a commercial software to study the flow past an aerofoil and then we will modify the aerofoil by adding a flap
Detailed information and step by-step-guides are contained in the documents “Getting started step-by-step” and “CFD CWM Journal File”
Detailed theoretical background is on the file “CWM handout”

## Slide 3
Contents
Welcome & housekeeping
Schedule for the week
Mode of assessment
Objectives of the CFD CWM
Practical briefs and design brief

## Slide 4
Welcome and housekeeping
Thanks for signing up to the CFD CWM
Generally speaking (except last day)
  Morning (9:00-12:00): short lecture/demonstration
  Afternoon (13:00-17:00): independent work/practice

## Slide 5
Schedule for the week
  Monday
    Morning: introduction to CFD methods, inviscid flows & practical aspects
    Afternoon: test drive
  Tuesday
    Morning: viscous setups
    Afternoon: numerical experiments
  Wednesday
    Morning: preparation for Friday assessment
    Afternoon: more experiments, parametric studies
  Thursday
    All day: independent work
  Friday
    Presentations & feedback

## Slide 6
Mode of assessment
  Assessment is by individual presentation
  Presentations will take place on Friday starting 2PM
  15 min. per student + 5 minutes questions
  Brief at the end of this presentation

## Slide 7
Objectives
  Fundamentals about discretization schemes
    What do the options the solver gives us actually mean?
  Running CFD solutions professionally
    Well documented and reproducible results
    Run efficiently
    Present useful information
  Awareness that nonsense is always around the corner – and how to avoid it!
  How to apply numerical techniques to design problems

## Slide 8
Learning Objectives
  Create a mesh for a simple geometry
  Import the mesh in a commercial CFD solver and setup a run
  Perform calculation
  Extract results
  Study systematically grid independence and robustness of the model

## Slide 9
What is CFD
CFD is a collection of techniques
Use computers
Produce approximate solutions to flow problems
It generally proceeds in the following steps
  Discretize the flow domain (meshing)
  Solve an approximate version of the Navier-Stokes on the discretised domain
    Approximations are both numerical (e.g. approximate differential operators)
    And physical (e.g. approximate the behaviour of turbulent flow without resolving turbulent structure)
  Interrogate the solution for quantities of interest/ assess accuracy

## Slide 10
Discretising the flow domain
Most CFD techniques are based on local solutions of the flow equations
Cannot be applied directly to an arbitrary flow domain
But can be applied to small subdomains of simple shape
  E.g. tetrahedra, prisms, pyramids, hexahedra
  A set of such small subdomains tessellating the flow domain is known as the mesh (or grid)
The collection of techniques used to subdivide a given flow domain into a set of small elements with “good” properties is known as mesh (or grid) generation

## Slide 11
Obtaining a solution
Once a flow domain is discretised a numerical solution can be obtained
What is required is a computer program, the “solver”
The solver has as input
  Information about the mesh (position of the nodes, how they are connected by the cells of the mesh, where are the boundaries)
  Information about the flow (fluid properties, boundary conditions, models, control parameters)
The output is the numerical solution
  A set of flow variables for each node (or cell)

## Slide 12
Interrogating a solution
Numerical solutions contain a fair amount of information
Extra information can be obtained by evaluating derived quantities
  E.g. wall shear stress or heat fluxes
Typcally, one can look at
  Integrals of fluxes on selected boundaries
    Mass flux
    Integrals of shear stress and normal stress at walls
  1D profiles
    Coefficients of pressure along lifting surfaces
  2D contours (or similar)
    Surface/space distributions of flow quantities

## Slide 13
Brief – Monday practical
Make sure you are familiar with
  Matlab scripts to generate grid
  Process to convert Plot3D files into CGNS files
  The Journal file
Make sure you know which file goes where and that you keep separate runs (journal file, mesh and results) in different folders
Tasks for today
  Find the panels in the interactive setup to set the CFL number, upwinding and numerical fluxes
  For an inviscid setup, study the effect of on the lift/incidence characteristic
    Grid resolution
    Domain size
  Study what happens at high incidence (30o). Is it what what you expect in an inviscid flow? Discuss why this is happening

## Slide 14
Brief – Tuesday practical
Familiarise yourself with the controls for viscous setups
Invoke the matlab scripts with the correct arguments to generate grids stretched towards the aerofoil wall
Tasks for today
  For a viscous setup with a turbulence model of your choice, study the effect of on the lift/incidence characteristic
    Grid resolution with particular attention to the wall resolution
    Domain size

## Slide 15
Brief – Wednesday practical
Familiarise yourself with the script to generate an aerofoil with flap
Setup a systematic study of the effect of flap geometric parameters on performance
Collect lift-drag data

## Slide 16
Finally your design brief!
This is a Gurney flap
Small triangular appendix near trailing edge
You see it sometimes on car spoilers
Operates by modifying the effective camber of an aerofoil
Increase lift (in most cases for down-force)
But also drag
ℓ
ℎ

## Slide 17
Presentation brief
Study inviscid flow on the un-modified NACA0012 aerofoil (Ma=0.1)
  Sensitivity of pressure coefficient to domain size (distance of airfoil surface to far-field boundary)
  Sensitivity of pressure coefficient to grid resolution
  Inviscid lift/incidence characteristic
  Discuss results at low incidence and high incidence
2) Study turbulent viscous flow on un-modified NACA0012 aerofoil (Ma=0.1, sea level standard air)
  Sensitivity of pressure and friction coefficient to grid resolution
  Lift/drag polar
  Compare to reference data (e.g. https://turbmodels.larc.nasa.gov/naca0012_val.html)
3) Parametric study of lift and drag characteristics of NACA0012 with Gurney flap with respect to flap chord and height at different incidence levels
  incidence (flap on the pressure side), ,
  When is the flap preferable to the clean aerofoil set at higher incidence?
This brief is not to rush you generate tons of numbers in two days
It is to give you a modicum of structure to organize your thoughts
And let you work in a relaxed and enjoyable manner
Variations are welcome, arm-waving is not

## Slide 18
Forces on a solid body immersed in a fluid
Force vector:
-component
-component
Where
is the perimeter of the aerofoil section
is the normal vector
is the tangent vector

## Slide 19
Forces on a solid body immersed in a fluid
Force vector:
Let’s stick to the inviscid contribution (pressure only)