## Slide 1: CWM CFD Presentation
Claudio Vestini – May 2024

## Slide 2: Introduction
Analysis of a NACA0012 aerofoil using CFD schemes, involving:
Method of finite volumes in Ansys Fluent
Implicit formulation
Second-order upwind discretisation
Addition of a Gurney Flap

## Slide 3: Inviscid Model 01.
Unmodified aerofoil
Analysis of model sensitivity to mesh topology (size and resolution)
Lift / Incidence characteristics

## Slide 4: Mesh Resolution
Coarse Mesh (0.1x)
Fine Mesh (10x)
Underpredicts pressure distribution
Can be expensive to run, better results
10° Incidence

## Slide 5: Domain Size
Small Domain (0.1x)
Large Domain (10x)
Not much difference…
10° Incidence

## Slide 6: Domain Size
…most sensitive zone is the stagnation point
Small domain gives a maximum 10% error
Large domain is 30% more accurate at predicting pressures around most critical point

## Slide 7: Lift / Incidence Characteristic
The model predicts stalling for an inviscid run… Nonsense!
21° Incidence

## Slide 8: Viscous Model 02.
K – ω RANS Model, Intensity of 5%, length scale of 0.02
Unmodified Aerofoil
Model sensitivity, lift/drag polar

## Slide 9: Mesh Resolution - Pressure
Not much change, most significant difference at top side around leading edge
A 0.1:1 scale coarser mesh will produce unreliable results (although this is unlikely to be implemented)
10° Incidence

## Slide 10: Mesh Resolution - Friction
Friction is more sensitive than Pressure to mesh resolution
For a viscous run, a fine mesh is much more effective at predicting the effects of boundary layers on shear stresses
Stagnation region experiences large du/dy

## Slide 11: Lift / Drag Polar
The polar curve is virtually Reynolds-independent for fully-developed flow
Use Ma = 0.3 to match NASA data (at Re = 6e6) on next slide
Re = 6.6e6
Re = 2.2e6

## Slide 12: Lift / Drag Polar
The Fluent results always predict a higher drag than NASA data
Likely due to numerical error in simulation
9° Incidence

## Slide 13: Gurney Flap 03.
Viscous K – ω Model
Analysis of flap performance at Low Incidence and High Incidence

## Slide 14: Low Incidence - Physics
Flap diverts streamlines upwards at the trailing edge, creating an updraft and a resultant downforce
This provides a nonzero (negative) lift at small angles of attack (including 0°)
Incidence of -3°
View of the Flap

## Slide 15: Low Incidence - Maths
A streamlined flap (aspect ratio of 1:1) produces extra lift at the expense of a small amount of drag – overall performance is better
A non-streamlined flap (high aspect ratio of 4:1) produces too much drag for a similar amount of lift – overall performance is worse
Aspect Ratio:
AR = h/l

## Slide 16: High Incidence - Physics
Flap has high pressure on the upstream side and low pressure on the downstream side
No flap
Flap
This generates an additional net drag force in the direction of the streamlines
Comparing this to the no-flap aerofoil, it will experience a smaller drag force
Incidence of -20°, Re = 3e5
View of the Flap

## Slide 17: High Incidence - Maths
The extra drag generated by the flap hinders performance
Since in stall conditions lift is very small, no geometry can offset this effect: gurney flap is detrimental at high incidence
Aspect Ratio:
AR = h/l